Hong Chi Corporate Co. LTD.

- LED Exit Sign Light

◎Features:

●Aluminum alloy and anodized frame, thin ,light and elegant.

●Using high-brightness SMD LED, small, low power consumption, and long life

●Single or double side are applicable. Easy install. Used on the wall, ceiling, and others.

●Advance light-guide technology, good uniformity and high quality. Optical materials maintain the colors.

●Suitable for AC 100V~ 220V. Charging 24 hours, emergent lighting more than 90 minutes.

●All series conform to National Fire Agency standards.

| Model | Label Sign | Specification | Size (mm) |
| --- | --- | --- | --- |
|  |  | Level | Battery Spec. | Light Spec. | Voltage | A | B | C |
| C150 | Single side Exit: A Left: B Right: C Two way: E Double side Single way: D Two way: DE | C | 3.6V/700mA | 0.07Ｗ/LED 8pcs | 85V-250V | 152 | 220 | 25 |
| C360 |  | C | 3.6V/900mA | 0.07Ｗ/LED 24pcs | 85V-250V | 362 | 190 | 25 |
| C500 |  | C | 3.6V/1300mA | 0.07Ｗ/LED 34pcs | 85V-250V | 502 | 240 | 25 |
| B200 |  | B | 3.6V/700mA | 0.07ＷLED14/28pcs | 85V-250V | 202 | 270 | 25 |
| B600 |  | B | 3.6V/1300mA | 0.07Ｗ/LED 40pcs | 85V-250V | 602 | 270 | 25 |
| B1000 |  | B | 3.6V/1300mA*2 | 0.07Ｗ/LED 68pcs | 85V-250V | 1002 | 270 | 25 |
| A400 |  | A | 7.2V/1700mA | 0.07Ｗ/LED 60pcs | 85V-250V | 402 | 470 | 25 |

# Text boxes

TEL:886-7-396-1226

FAX:886-7-396-1225